## Slide 1: BliMe: Verifiably Secure Outsource Computation with Hardware-Enforced Taint Tracking
Hossam ElAtali, Lachlan J. Gunn, Hans Liljestrand, N. Asokan
elatalhm.github.io

## Slide 2: Scenario: outsourced computation
Goal: run the server’s confidential code over client’s confidential data
  Initial target: Outsourced ML inference and/or training
How can the client avoid revealing data to the service provider?
  Fully-Homomorphic Encryption: slow due to computational overhead
  Multi-Party Computation: slow due to network overhead
  Hardware-based isolation + remote attestation: fast
Client
Server
Secret
Secret
2

## Slide 3: Scenario: outsourced computation
Goal: run the server’s confidential code over client’s confidential data
  Initial target: Outsourced ML inference and/or training
How can the client avoid revealing data to the service provider?
  Fully-Homomorphic Encryption: slow due to computational overhead
  Multi-Party Computation: slow due to network overhead
  Hardware-based isolation + remote attestation: fast
Client
Server
2

## Slide 4: Scenario: outsourced computation
Goal: run the server’s confidential code over client’s confidential data
  Initial target: Outsourced ML inference and/or training
How can the client avoid revealing data to the service provider?
  Fully-Homomorphic Encryption: slow due to computational overhead
  Multi-Party Computation: slow due to network overhead
  Hardware-based isolation + remote attestation: fast
Client
Server
Server sees sensitive data
2

## Slide 5: Scenario: outsourced computation
Goal: run the server’s confidential code over client’s confidential data
  Initial target: Outsourced ML inference and/or training
How can the client avoid revealing data to the service provider?
  Fully-Homomorphic Encryption: slow due to computational overhead
  Multi-Party Computation: slow due to network overhead
  Hardware-based isolation + remote attestation: fast
Client
Server
Server sees sensitive data
Result
2

## Slide 6: Scenario: outsourced computation
Goal: run the server’s confidential code over client’s confidential data
  Initial target: Outsourced ML inference and/or training
How can the client avoid revealing data to the service provider?
  Fully-Homomorphic Encryption: slow due to computational overhead
  Multi-Party Computation: slow due to network overhead
  Hardware-based isolation + remote attestation: fast
Client
Server
Server sees sensitive data
Result
2

## Slide 7: Scenario: outsourced computation
Goal: run the server’s confidential code over client’s confidential data
  Initial target: Outsourced ML inference and/or training
How can the client avoid revealing data to the service provider?
  Fully-Homomorphic Encryption: slow due to computational overhead
  Multi-Party Computation: slow due to network overhead
  Hardware-based isolation + remote attestation: fast
Client
Server
Server sees sensitive data
Result
2

## Slide 8: Scenario: outsourced computation
Goal: run the server’s confidential code over client’s confidential data
  Initial target: Outsourced ML inference and/or training
How can the client avoid revealing data to the service provider?
  Fully-Homomorphic Encryption: slow due to computational overhead
  Multi-Party Computation: slow due to network overhead
  Hardware-based isolation + remote attestation: fast
Client
Server
Server sees sensitive data
Result
2

## Slide 9: Protection provided by TEEs comes with caveats
TEEs provide an isolated environment for execution of software
TEEs are unsuitable when server code is confidential or unverifiable
  TEEs intended for clients to run code they trust and can verify
Confidentiality of client data in TEEs is hampered by:
Large TEE code base → vulnerable to software flaws
Sharing resources → vulnerable to side channels
3

## Slide 10: Protection provided by TEEs comes with caveats
TEEs provide an isolated environment for execution of software
TEEs are unsuitable when server code is confidential or unverifiable
  TEEs intended for clients to run code they trust and can verify
Confidentiality of client data in TEEs is hampered by:
Large TEE code base → vulnerable to software flaws
Sharing resources → vulnerable to side channels
3

## Slide 11: Protection provided by TEEs comes with caveats
TEEs provide an isolated environment for execution of software
TEEs are unsuitable when server code is confidential or unverifiable
  TEEs intended for clients to run code they trust and can verify
Confidentiality of client data in TEEs is hampered by:
Large TEE code base → vulnerable to software flaws
Sharing resources → vulnerable to side channels
3

## Slide 12: Is Confidentiality vs. Performance a tradeoff?
High
performance
Low
performance
Low confidentiality
High confidentiality
+ current TEEs
Vanilla outsourced computing
Fully-Homomorphic Encryption
4

## Slide 13: Is Confidentiality vs. Performance a tradeoff?
High
performance
Low
performance
Low confidentiality
High confidentiality
+ current TEEs
Vanilla outsourced computing
Fully-Homomorphic Encryption
Our goal
4
Notes: Mention “leveraging HW assistance”

## Slide 14: What can be done?
Prevent application software from leaking sensitive data
  Use hardware-assisted taint-tracking
  Need not verify trustworthiness of application s/w
Minimize resource sharing
  Move critical operations to a fixed-function, isolated module (HSM)
  All HSM code analyzed in advance, guaranteed not to be malicious
5
Notes: HW-assistance
Critical ops e.g. key management, remote attestation

## Slide 15: Prevent leakage of sensitive data via CPU extensions
“Safe” streams of instructions don’t expose sensitive data
Allowed:
  Computation on sensitive data by arbitrary, unattested, untrusted software
Prohibited:
  Leaking sensitive data into any observable state, e.g.: peripherals outside security boundary, microarchitectural state
Use taint-tracking-based security policy to limit sensitive data to safe places
6

## Slide 16: Combine with attestable HSM to assure clients
Remote attestation assures use of client data is subject to security policy
Client
Server
CPU extensions + fixed-function HSM
Application S/W
7
Notes: RA: 1) Genuine TEE with proper key management. 2) Taint-tracking and security policies are enforced by main CPU

## Slide 17: Combine with attestable HSM to assure clients
Remote attestation assures use of client data is subject to security policy
Client
Server
CPU extensions + fixed-function HSM
Application S/W
7
Notes: RA: 1) Genuine TEE with proper key management. 2) Taint-tracking and security policies are enforced by main CPU

## Slide 18: Combine with attestable HSM to assure clients
Remote attestation assures use of client data is subject to security policy
Client
Server
CPU extensions + fixed-function HSM
Application S/W
Blinded
7
Notes: RA: 1) Genuine TEE with proper key management. 2) Taint-tracking and security policies are enforced by main CPU

## Slide 19: Combine with attestable HSM to assure clients
Remote attestation assures use of client data is subject to security policy
Client
Server
CPU extensions + fixed-function HSM
Application S/W
Blinded
7
Notes: RA: 1) Genuine TEE with proper key management. 2) Taint-tracking and security policies are enforced by main CPU

## Slide 20: Combine with attestable HSM to assure clients
Remote attestation assures use of client data is subject to security policy
Client
Server
CPU extensions + fixed-function HSM
Application S/W
Blinded
7
Notes: RA: 1) Genuine TEE with proper key management. 2) Taint-tracking and security policies are enforced by main CPU

## Slide 21: Combine with attestable HSM to assure clients
Remote attestation assures use of client data is subject to security policy
Client
Server
CPU extensions + fixed-function HSM
Application S/W
7
Notes: RA: 1) Genuine TEE with proper key management. 2) Taint-tracking and security policies are enforced by main CPU

## Slide 22: Combine with attestable HSM to assure clients
Remote attestation assures use of client data is subject to security policy
Client
Server
CPU extensions + fixed-function HSM
Application S/W
7
Notes: RA: 1) Genuine TEE with proper key management. 2) Taint-tracking and security policies are enforced by main CPU

## Slide 23: How does this taint-tracking policy work?
8

## Slide 24: Taint tracking policy
Registers/memory have an associated “sensitive” bit (“Blinded“)
Ideal rule:
Blinded(outputm) ← ∃n,m: Blinded(inputₙ) ∧ Depends(outputm on inputₙ)
Goal: changes in state never affect
9
Notes: Mention that we’ll explain what’s forbidden in more detail later

## Slide 25: Taint tracking policy
Registers/memory have an associated “sensitive” bit (“Blinded“)
Ideal rule:
Blinded(outputm) ← ∃n,m: Blinded(inputₙ) ∧ Depends(outputm on inputₙ)
Goal: changes in sensitive state never affect non-sensitive state
9
Notes: Mention that we’ll explain what’s forbidden in more detail later

## Slide 26: Taint tracking policy
Registers/memory have an associated “sensitive” bit (“Blinded“)
Ideal rule:
Blinded(outputm) ← ∃n,m: Blinded(inputₙ) ∧ Depends(outputm on inputₙ)
Goal: changes in sensitive state never affect non-sensitive state
Register A
Register B
Blinded = 1
9
Notes: Mention that we’ll explain what’s forbidden in more detail later

## Slide 27: Taint tracking policy
Registers/memory have an associated “sensitive” bit (“Blinded“)
Ideal rule:
Blinded(outputm) ← ∃n,m: Blinded(inputₙ) ∧ Depends(outputm on inputₙ)
Goal: changes in sensitive state never affect non-sensitive state
instn out A, in B, in A
Register A
Register B
Blinded = 1
9
Notes: Mention that we’ll explain what’s forbidden in more detail later

## Slide 28: Taint tracking policy
Registers/memory have an associated “sensitive” bit (“Blinded“)
Ideal rule:
Blinded(outputm) ← ∃n,m: Blinded(inputₙ) ∧ Depends(outputm on inputₙ)
Goal: changes in sensitive state never affect non-sensitive state
instn out A, in B, in A
Register A
Register B
Blinded = 1
Blinded = 1
9
Notes: Mention that we’ll explain what’s forbidden in more detail later

## Slide 29: Taint tracking policy
Registers/memory have an associated “sensitive” bit (“Blinded“)
Ideal rule:
Blinded(outputm) ← ∃n,m: Blinded(inputₙ) ∧ Depends(outputm on inputₙ)
Goal: changes in sensitive state never affect non-sensitive state
instn out A, in B, in A
instn out A
Register A
Register B
Blinded = 1
Blinded = 1
9
Notes: Mention that we’ll explain what’s forbidden in more detail later

## Slide 30: Taint tracking policy
Registers/memory have an associated “sensitive” bit (“Blinded“)
Ideal rule:
Blinded(outputm) ← ∃n,m: Blinded(inputₙ) ∧ Depends(outputm on inputₙ)
Goal: changes in sensitive state never affect non-sensitive state
instn out A, in B, in A
instn out A
Register A
Register B
Blinded = 1
9
Notes: Mention that we’ll explain what’s forbidden in more detail later

## Slide 31: Thinking beyond registers and memory
Taint-propagation rule must consider many different observable outputs
  Registers
  Memory values
  Control flow
10

## Slide 32: Thinking beyond registers and memory
Taint-propagation rule must consider many different observable outputs
  Registers
  Memory values
  Control flow
10

## Slide 33: Taint tracking policy
Registers/memory have an associated “sensitive” bit (“Blinded“)
Ideal rule:
Blinded(outputm) ← ∃n,m: Blinded(inputₙ) ∧ Depends(outputm on inputₙ)
Goal: changes in sensitive state never affect non-sensitive state
Register A
Register B
Blinded = 1
jmp in B
PC
11
Notes: Mention that we’ll explain what’s forbidden in more detail later

## Slide 34: Taint tracking policy
Registers/memory have an associated “sensitive” bit (“Blinded“)
Ideal rule:
Blinded(outputm) ← ∃n,m: Blinded(inputₙ) ∧ Depends(outputm on inputₙ)
Goal: changes in sensitive state never affect non-sensitive state
Register A
Register B
Blinded = 1
jmp in B
PC
11
Notes: Mention that we’ll explain what’s forbidden in more detail later

## Slide 35: Taint tracking policy
Registers/memory have an associated “sensitive” bit (“Blinded“)
Ideal rule:
Blinded(outputm) ← ∃n,m: Blinded(inputₙ) ∧ Depends(outputm on inputₙ)
Goal: changes in sensitive state never affect non-sensitive state
Register A
Register B
Blinded = 1
jmp in B
PC
11
Notes: Mention that we’ll explain what’s forbidden in more detail later

## Slide 36: Taint tracking policy
Registers/memory have an associated “sensitive” bit (“Blinded“)
Ideal rule:
Blinded(outputm) ← ∃n,m: Blinded(inputₙ) ∧ Depends(outputm on inputₙ)
Goal: changes in sensitive state never affect non-sensitive state
Register A
Register B
Blinded = 1
jmp in B
PC
Cannot become blinded
11
Notes: Mention that we’ll explain what’s forbidden in more detail later

## Slide 37: Thinking beyond registers and memory
Taint-propagation rule must consider many different observable outputs
  Registers
  Memory values
  Control flow
  Exceptions
  Memory access patterns
Not all of these outputs can be marked as sensitive
Data flows from sensitive values to “un-markable” outputs must yield a fault
12

## Slide 38: Thinking beyond registers and memory
Taint-propagation rule must consider many different observable outputs
  Registers
  Memory values
  Control flow
  Exceptions
  Memory access patterns
Not all of these outputs can be marked as Blinded
Data flows from sensitive values to “un-markable” outputs must yield a fault
12

## Slide 39: Thinking beyond registers and memory
Taint-propagation rule must consider many different observable outputs
  Registers
  Memory values
  Control flow
  Exceptions
  Memory access patterns
Not all of these outputs can be marked as Blinded
Data flows from Blinded values to “un-markable” outputs must yield a fault
12

## Slide 40: Putting it all together…
13

## Slide 41: BliMe Architecture
Handshake (incl. remote attestation)
Shared secret key
Atomic data import (inputs)
  Decrypt & blind (Blinded ← true)
Safe (“blinded”) computation
  Enforced by BliMe HW extensions
Atomic data export (result)
  Encrypt & unblind (Blinded ← false)
HSM
Blinded
Server
14
Notes: Main CPU contains an encryption engine. Encryption engine provides 2 atomic operations: decrypt-and-blind and encrypt-and-unblind

## Slide 42: BliMe Architecture
Handshake (incl. remote attestation)
Shared secret key
Atomic data import (inputs)
  Decrypt & blind (Blinded ← true)
Safe (“blinded”) computation
  Enforced by BliMe HW extensions
Atomic data export (result)
  Encrypt & unblind (Blinded ← false)
CPU with our extensions
HSM
Blinded
Server
14
Notes: Main CPU contains an encryption engine. Encryption engine provides 2 atomic operations: decrypt-and-blind and encrypt-and-unblind

## Slide 43: BliMe Architecture
Handshake (incl. remote attestation)
Shared secret key
Atomic data import (inputs)
  Decrypt & blind (Blinded ← true)
Safe (“blinded”) computation
  Enforced by BliMe HW extensions
Atomic data export (result)
  Encrypt & unblind (Blinded ← false)
Fixed-function HSM
CPU with our extensions
HSM
Blinded
Server
14
Notes: Main CPU contains an encryption engine. Encryption engine provides 2 atomic operations: decrypt-and-blind and encrypt-and-unblind

## Slide 44: BliMe Architecture
Handshake (incl. remote attestation)
Shared secret key
Atomic data import (inputs)
  Decrypt & blind (Blinded ← true)
Safe (“blinded”) computation
  Enforced by BliMe HW extensions
Atomic data export (result)
  Encrypt & unblind (Blinded ← false)
Fixed-function HSM
CPU with our extensions
HSM
Blinded
Server
14
Notes: Main CPU contains an encryption engine. Encryption engine provides 2 atomic operations: decrypt-and-blind and encrypt-and-unblind

## Slide 45: BliMe Architecture
Handshake (incl. remote attestation)
Shared secret key
Atomic data import (inputs)
  Decrypt & blind (Blinded ← true)
Safe (“blinded”) computation
  Enforced by BliMe HW extensions
Atomic data export (result)
  Encrypt & unblind (Blinded ← false)
Fixed-function HSM
CPU with our extensions
HSM
Blinded
Server
14
Notes: Main CPU contains an encryption engine. Encryption engine provides 2 atomic operations: decrypt-and-blind and encrypt-and-unblind

## Slide 46: BliMe Architecture
Handshake (incl. remote attestation)
Shared secret key
Atomic data import (inputs)
  Decrypt & blind (Blinded ← true)
Safe (“blinded”) computation
  Enforced by BliMe HW extensions
Atomic data export (result)
  Encrypt & unblind (Blinded ← false)
Fixed-function HSM
CPU with our extensions
HSM
Blinded
Server
14
Notes: Main CPU contains an encryption engine. Encryption engine provides 2 atomic operations: decrypt-and-blind and encrypt-and-unblind

## Slide 47: BliMe Architecture
Handshake (incl. remote attestation)
Shared secret key
Atomic data import (inputs)
  Decrypt & blind (Blinded ← true)
Safe (“blinded”) computation
  Enforced by BliMe HW extensions
Atomic data export (result)
  Encrypt & unblind (Blinded ← false)
Fixed-function HSM
CPU with our extensions
HSM
Blinded
Server
14
Notes: Main CPU contains an encryption engine. Encryption engine provides 2 atomic operations: decrypt-and-blind and encrypt-and-unblind

## Slide 48: BliMe-BOOM Implementation
On speculative OoO RISC-V BOOM core
Tagged memory: each word can be marked as blinded
  Blinded or non-Blinded
Implements taint-tracking for all instructions
  Blinded(outputs) ← Blinded(input₁) ∨ Blinded(input₂) ∨ …
15

## Slide 49: BliMe-BOOM Implementation
On speculative OoO RISC-V BOOM core
Tagged memory: each word can be marked as blinded
Instructions to mark physical memory as
  Blinded or non-Blinded
Implements taint-tracking for all instructions
  Blinded(outputs) ← Blinded(input₁) ∨ Blinded(input₂) ∨ …
15

## Slide 50: BliMe-BOOM Implementation
On speculative OoO RISC-V BOOM core
Tagged memory: each word can be marked as blinded
Instructions to mark physical memory as
  Blinded or non-Blinded
Implements taint-tracking for all instructions
  Blinded(outputs) ← Blinded(input₁) ∨ Blinded(input₂) ∨ …
15

## Slide 51: BliMe-BOOM Implementation
On speculative OoO RISC-V BOOM core
Tagged memory: each word can be marked as blinded
Instructions to mark physical memory as
  Blinded or non-Blinded
Implements taint-tracking for all instructions
  Blinded(outputs) ← Blinded(input₁) ∨ Blinded(input₂) ∨ …
instr
15
Notes: Mention approximation

## Slide 52: Speculative out-of-order execution
Same security policy enforced during speculation
Instructions causing side-channel leakage (even speculatively) will fault
Blindedness must be tracked throughout the processor microarchitecture
  Registers, load/store queue entries, line fill buffers, etc.
  Ensured by Chisel RTL type system
16

## Slide 53: Handling multiple clients simultaneously
So far, one Blinded bit for many clients
  Server can send sensitive data to the wrong client
We need a separate sensitivity domain for each client
  Prevent clients accessing each other’s sensitive data
  Keys need to be swapped in and out for each client
Solution: Hardware support
  Hardware keeps track of sensitivity domains: multibit Blindedness tag
  Secure despite malicious OS
17

## Slide 54: Handling multiple clients simultaneously
So far, one Blinded bit for many clients
  Server can send sensitive data to the wrong client
We need a separate sensitivity domain for each client
  Prevent clients accessing each other’s sensitive data
  Keys need to be swapped in and out for each client
Solution: Hardware support
  Hardware keeps track of sensitivity domains: multibit Blindedness tag
  Secure despite malicious OS
17

## Slide 55: Handling multiple clients simultaneously
So far, one Blinded bit for many clients
  Server can send sensitive data to the wrong client
We need a separate sensitivity domain for each client
  Prevent clients accessing each other’s sensitive data
  Keys need to be swapped in and out for each client
Solution: Hardware support
  Hardware keeps track of sensitivity domains: multibit Blindedness tag
  Secure despite malicious OS
17

## Slide 56: Evaluation
Compatibility: Tested with side-channel-resistant crypto library (TweetNaCl)
  Side-channel-resistant crypto runs without modifications
Overheads:
Type | ∆
LUTs & Registers | +9.0%
Power | +1.4%
Performance (SPEC17) | +8%
FPGA
FPGA
gem5
18
Notes: We show that code that is already side-channel-resistant runs without issue

## Slide 57: Security: Formal verification in F*
Goal: changes in blinded state never affect non-blinded state
(*******************************************************************************
* Equivalence-based safety.
*
* We define safety in this case to be that the system is safe if executing on
* equivalent (and so indistinguishable) states always results in equivalent
* output states.
*******************************************************************************)
let equivalent_inputs_yield_equivalent_states (exec:execution_unit) (pre1 pre2 : systemState) =
equiv_system pre1 pre2 ⇒ equiv_system (step exec pre1) (step exec pre2)
let is_safe (exec:execution_unit) =
∀ (pre1 pre2 : systemState). equivalent_inputs_yield_equivalent_states exec pre1 pre2
https://blinded-computation.github.io/blime-model/
19

## Slide 58: Generating compliant code with LLVM
Problem: software might not run as-is
  BliMe hardware extensions will abort non-compliant code
Creating compliant code by hand is error prone
  High-level verification often insufficient
  Challenge exacerbated due to obtuse compiler behavior
  Usability/deployability challenge, not security
Challenge: solutions like Constantine[B+21] are not applicable as-is
  Uses dynamic profiling; under-approximates taint (best-effort approach)
[B+21] "Constantine: Automatic Side-Channel Resistance Using Efficient Control and Data Flow Linearization”, ACM CCS (2021)
TensorFlow Lite hand-ported to run on BliMe
20

## Slide 59: Generating compliant code with LLVM
Problem: software might not run as-is
  BliMe hardware extensions will abort non-compliant code
Creating compliant code by hand is error prone
  High-level verification often insufficient
  Challenge exacerbated due to obtuse compiler behavior
  Usability/deployability challenge, not security
Challenge: solutions like Constantine[B+21] are not applicable as-is
  Uses dynamic profiling; under-approximates taint (best-effort approach)
[B+21] "Constantine: Automatic Side-Channel Resistance Using Efficient Control and Data Flow Linearization”, ACM CCS (2021)
TensorFlow Lite hand-ported to run on BliMe
Ongoing work
20

## Slide 60: Summary
BliMe provides FHE-style security, but efficiently
Safely run untrusted code on sensitive data
Implemented for BOOM (speculative OoO CPU core)
Ongoing work: compiler support for usability
Paper, source code, formal model
ssg-research.github.io /platsec/blime/
21

## Slide 62: How to deal with exceptions
Examples of data-dependent exceptions:
  Division by zero
  Floating-point exceptions
  …
Instructions must not raise an exception based on data-dependent conditions
Solutions:
  Unconditional faults (i.e., division by sensitive values always fails)
  Set a sensitive error flag and continue computation

## Slide 63: Handling multiple clients simultaneously
Solution 1: BliMe-BOOM-1 + Isolation by honest-but-curious server OS
  OS keeps track of sensitivity domains
  Requires only single Blinded bit from HW: low memory overhead
  Rely on remote attestation of the entire OS to convince client
Solution 2: BliMe-BOOM-N -- Hardware support for multiple clients
  Hardware keeps track of sensitivity domains: multibit Blindedness tag
  Secure despite malicious OS
  Needs extra memory/logic to keep track of domain identifier for each granule
Notes: After this slide, transition to implementation

## Slide 64: Generating compliant code with LLVM: our solution
Solution: Use static analysis to propagate taint
  Trade-off: over-approximation
Use SVF[S+16] as a starting point
SVF provides static value-flow graph
  Shows value dependencies within program
Identify and transform potential violations
  Apply data- and control-flow linearization
[S+16] "SVF: interprocedural static value-flow analysis in LLVM”, ACM International Conference on Compiler Construction (2016)

## Slide 65: Control-flow linearization
Control-flow decisions can leak data
  Timing, cache, branch predictor side channels
Linearization allows “branching” code
  Executes all branches but keeps only desired results
if (secret) { // affects branch predictor
arr[0] = X; // affects cache
} else {
arr[1] = X; // affects cache
}
taken = secret;
// if block always executed
old = arr[0];
arr[0] = (taken ? X : old);
// else block always executed
old = arr[1];
arr[1] = (!taken ? X : old);

## Slide 66: Data-flow linearization
Memory accesses can leak information
  Secret-dependent memory access can leak information through side-channels
Linearization removes data-dependence
  Always access each cache line
  stride = cacheLineSize
Array
0
1
2
3
4
5
Cache line size
Array
0
1
2
3
4
5
Cache line size
Offset